## Slide 1: Verifying the SHA-3 Implementation from OpenSSL with the Software Analysis Workbench
P. Hanson*, B. Winters, E. Mercer, and B. Decker
Brigham Young University
SPIN 2022
Notes: My name is Parker Hanson, and I’m an adult.
My dad ain’t a cell phone.

## Slide 2
Cryptol Language of Cryptography
Galois Software Analysis Workbench (SAW)
Notes: What is cryptol?
What is SAW?

## Slide 3
Relies on SHA-2 so a verified library is needed
Notes: Galois used SAW to prove HMAC and other crypto structures to be correct.
The HMAC proof assumes correctness of the SHA2 algorithm

## Slide 4
Proved out OpenSSL’s SHA-2 with SAW, but what about modern algorithms for digests?
Notes: SHA-2 is a compression-based algorithm.
It is not modular, so it had to be decomposed to be proved out in SAW.
Each decomposed piece shown equivalent to a Cryptol specification.
Use overrides to replace decomposed piece with the Cryptol.
Reduced the complexity of the proof of equivalence to a Cryptol specification for SHA-2.
What about SHA-2.
The sponge construction is inherently more modular so it should lend itself better to SAW---no need for a decomposition.

## Slide 5: SHA-3 Sponge Construction
func SHA-3(N,d,r) returns D
1: p0,…,pm = pad(N,r)
2: A = 00,…,01599
3: for pi = p0,…,pm do
4: A = A xor zeroExtend(pi,a-r)
5: A = Keccak(A)
6: end for
7: D = take(A,d)
Absorb r bits
Squeeze d bits
Partition to r-bit blocks
Notes: n ≥ 0 and (d, r) ∈ {(224, 1152) (256, 1088) (384, 832) (512, 576)}
With d=digest_size, r=rate, n=input_size
VERIFY ^
SHA3 handles its input differently from its predecessors.
<Possible description of sponge?>

## Slide 6: Keccak Transformation Function
Parity over Columns
Input: 5 x 5 array of 64-bit words (1600 bits)
Output: input transformed by 5 successive functions
Bitwise rotate
Permutation
Row combination
Constant mix in
Notes: Keccak consists of five functions.
Each function performs an independent state transformation.

## Slide 7
A = Keccak(A)
Wt =
pit
1(Wt-2) + Wt-7 + (Wt-15) + Wt-16
a, b, c, d, e, f, g, h =
H0(i-1), H1(i-1), H2(i-1), H3(i-1), H4(i-1), H5(i-1), H6(i-1), H7(i-1)
for t = 0 to 63:
T1 = h + ∑(e) + Ch(e,f,g) + Kt + Wt
T2 = ∑(a) + Maj(a,b,c)
a, b, c, d, e, f, g, h =
g, f, e, d + T1, c, b, a, T1 + T2
end for
H0(i), H1(i), H2(i), H3(i), H4(i), H5(i), H6(i), H7(i) =
a + H0(i-1), b + H1(i-1), c + H2(i-1), d + H3(i-1),
e + H4(i-1), f + H5(i-1), g + H6(i-1), h + H7(i-1)
H0(m)·H1(m)·H2(m)·H3(m)·H4(m)·H5(m)·H6(m)·H7(m)
A = A xor zeroExtend(pi,a-r)
D = take(A,d)
SHA-3
SHA-2
Notes: Sponge construction versus compression-based construction in SHA-2
<What differences should we focus on?>

## Slide 8
Modularity of SHA-3 should make it easier to verify in SAW because of overrides
Notes: Through SAW’s override system and KECCAK’s modular layout, we were able to prove each of the five functions individually.
With those resulting contracts we proved the entirety of KECCAK.

## Slide 9: Write a Cryptol Specification for SHA-3
For all triples (x,y,z) such that
0 <= x < 5, 0 <= y < 5, and 0 <= z < w,
Let A’[x,y,z] = A[(x + 3y) mod 5, x, z]
pi a =
for LIST4 (\x ->
for LIST4 (\y ->
for LIST63 (\z ->
a @((x + 3*y) % 5) @x @z)))
pi a =
[ [ [ a @((x + 3*y) % 5) @x @z
| z <- [0..63]]
| y <- [0..4]]
| x <- [0..4]]
Without for-macro
With for-macro
Created similar macro for while-loops
Notes: Visual inspection with the standard Cryptol syntax of list comprehensions was not always intuitive.
We constructed higher order functions that hide the less comparable list comprehensions to greatly simplify looping structures such as for and while loops.
This led to a more straightforward visual comparison.

## Slide 10: Argue Specification matches NIST
NIST
Standard (256)
Keccak
English
SPEC (256)
Keccak
CRY
Visual Inspection
Test Vectors
Around 200 Lines of Cryptol to ponder and compare
Notes: Since the NIST standard is written in a document, visual inspection is impossible to avoid.
By leveraging our higher-order functions we produced a visually comparable Cryptol implementation of SHA3.
We also relied on the provided NIST test vectors for additional assurance of correctness.

## Slide 11: Address C Memory Layout
Cartesian 5 x 5 x 64 bits
A[x,y,z]: xth col, yth row, zth bit
uint64_t A[5][5]
A[x,y]: word at xth row, yth col
VERSUS
OpenSSL (256)
Keccak
CRY
SPEC (256)
Keccak
CRY
Brute Force 60 hrs
Computed Constants
Lookup Table
Verified 0 to 1,088 bit message sizes to cover all padding scenarios
Notes: OpenSSL’s C implementation formatted the intermediate state differently from the NIST standard.
A direct comparison from our visually reviewable Cryptol implementation to the OpenSSL implementation was too complex to complete with SAW.
Because Cryptol is natively supported in SAW, Cryptol to Cryptol comparisons are more feasible.
We produced a second Cryptol implementation that followed the OpenSSL’s memory layout and proved the equivalence between the two Cryptol implementations.
Due to differences in memory, this was done at the top level of the SHA3 algorithm.
Strict typing constraints required us to verify for each critical input message size.
By verifying all message lengths from 0 to 1088 bits, all possible padding inputs, we covered every conceivable branch.

## Slide 12: Focus on Keccak
OpenSSL (256)
Keccak
C
SPEC (256)
Keccak
CRY
Keccak
Keccak
Prove Equivalent
Too big to prove equivalent
Notes: <What should we cover here?>

## Slide 13: Prove Keccak equivalence with overrides
Keccak
Keccak
Too complex to prove equivalent
Notes: Keccak was too difficult to prove, yet due to its modularity we could prove each of the inner functions individually.

## Slide 14: Prove Functions Equivalent to OpenSSL C
Equal for all input
Equal for all input
Equal for all input
Equal for all input
Equal for all input
Cryptol
C Code
Notes: Each smaller transformation function was compared and shown equivalent.

## Slide 15: Prove Keccak equivalence with overrides
Prove Equivalent
Keccak
Keccak
Notes: Through SAW overrides, we lessened the complexity of the generated computational models.
This allowed the solver to complete within a reasonable time.